## Slide 1: CompTIA A+ Guide to IT Technical Support
10th Edition

## Slide 2: Supporting Hard Drives and Other Storage Devices
Chapter 5

## Slide 3: Objectives
Describe and contrast technologies used inside a hard drive and how a computer communicates with a hard drive
Select, install, and support a hard drive
Identify tape drives and tape cartridges
Support optical drives, solid-state storage, and flash memory devices
Troubleshoot hard drives

## Slide 4: Hard Drive Technologies and Interface Standards
A hard disk drive (HDD) is rated by its:
  Physical size
  Capacity
  Speed
  Technologies used inside the drive
  Interface standards

## Slide 5: Technologies and Form Factors of Hard Drives (1 of 7)
Two types of hardware technologies used inside the drive are magnetic and solid-state
Magnetic Hard Drives
  One, two, or more platters, or disks
    Stacked together, spinning in unison inside a sealed metal housing
  Firmware controls data reading, writing and motherboard communication
  Read/write heads are controlled by an actuator
  Data is organized in concentric circles, called tracks
    Tracks are divided into segments called sectors
  Most current drives use 4096-byte sectors
  Form factors for internal magnetic hard drives are 3.5” for desktops and 2.5” for laptop computers

## Slide 6: Technologies and Form Factors of Hard Drives (2 of 7)
Figure 5-1 Inside a magnetic hard drive

## Slide 7: Technologies and Form Factors of Hard Drives (3 of 7)
Figure 5-3 A magnetic hard drive for a desktop is larger than that used in laptops

## Slide 8: Technologies and Form Factors of Hard Drives (4 of 7)
Solid-state drive (SSD)
  Also called a solid-state device
  No moving parts
  Built using nonvolatile memory, similar to that used for USB flash drives
  Memory in an SSD is called NAND flash memory
  Life span is based on the number of write operations to the drive
    Expressed as TBW (TeraBytes Written) or DWPD (Drive Writes Per Day)
  Solid-state drives are more expensive than magnetic hard drives, but they are faster, more reliable, last longer, and use less power than magnetic drives
  Three popular form factors used by SSDs:
    2.5” SSD, M.2 SSD card, and PCI Express SSD expansion card

## Slide 9: Technologies and Form Factors of Hard Drives (5 of 7)
Figure 5-5 Solid-state drives in two form factors: 2.5” SSD and two lengths of M.2 SSD cards

## Slide 10: Technologies and Form Factors of Hard Drives (6 of 7)
Hybrid Hard Drives
  A hybrid hard drive (H-HDD) is sometimes called a solid-state hybrid drive (SSHD)
  Contains both magnetic and SSD technologies
  The magnetic drive in the housing permanently holds data
  The flash component serves as a buffer to improve drive performance
  The operating system must support a hybrid drive in order for it to function
Logical Block Addressing and Capacity
  Low-level formatting – sector markings are written to the hard drive at the factory
    Not the same as high-level formatting performed for Operating System installation
  Firmware, BIOS/UEFI, and the OS use logical block addressing (LBA) to address all hard drive sectors
    Size of each block + total number of blocks determine drive capacity

## Slide 11: Technologies and Form Factors of Hard Drives (7 of 7)
S.M.A.R.T.
  S.M.A.R.T. (Self-Monitoring Analysis ad Reporting Technology) is used to predict when a drive is likely to fail
  System BIOS/UEFI uses S.M.A.R.T. to monitor:
    Drive performance, temperature, and other factors
  For magnetic drives, it monitors:
    Disk spin-up time, distance between the head and the disk, other mechanical activities of the drive
  If S.M.A.R.T. suspects a drive failure is about to happen, it displays a warning message
  It can be enabled and disabled in BIOS/UEFI setup

## Slide 12: Interface Standards Used by Hard Drives (1 of 11)
Four interface standards used by hard drives include:
  IDE (outdated)
  SCSI (outdated)
  SATA
  NVMe
IDE
  Also known as the Parallel ATA (PATA) standards
  Allowed for one or two IDE connectors on a motherboard using a 40-pin data cable
  Two types of IDE cables are the older cable with a 40-pin connector with 40 wires and a newer cable with the same 40-pin connector and 80 thinner wires
  The maximum recommended length of an IDE cable is 18”

## Slide 13: Interface Standards Used by Hard Drives (2 of 11)
Figure 5-8 In comparing the 80-conductor cable with the 40-conductor cable, note they are about the same width, but the 80-conductor cable has twice as many fine wires

## Slide 14: Interface Standards Used by Hard Drives (3 of 11)
SCSI
  In the past, hard drives designed for high-end workstations used the SCSI (Small Computer System Interface) interface standard
  SCSI can support up to 7 or 15 SCSI-compliant devices in a system
  A SCSI expansion card, called the SCSI host adapter, used a PCIe slot and provided one external connector for an external SCSI device and one internal connector for internal SCSI devices

## Slide 15: Interface Standards Used by Hard Drives (4 of 11)
Figure 5-10 This 68-pin internal SCSI ribbon cable can connect several SCSI devices

## Slide 16: Interface Standards Used by Hard Drives (5 of 11)
SATA
  Most hard drives today use the serial ATA or SATA interface standard
  SATA uses a serial data path
  A SATA data cable can accommodate a single SATA drive
  Three SATA standards:
    SATA3 or SATA III
    SATA2 or SATA II
    SATA1 or SATA I
  SATA standards are used by all drive types
    Supports hot-swapping (hot-plugging)
      Can connect and disconnect a drive while system is running
    Connects to one internal SATA connector on the motherboard via a 7-pin data cable
      Uses a 15-pin SATA power connector
    A motherboard might have two or more SATA connectors
      Use connectors in the order recommended in the motherboard user guide

## Slide 17: Interface Standards Used by Hard Drives (6 of 11)
Figure 5-11 A SATA cable connects a single SATA drive to a motherboard SATA connector

## Slide 18: Interface Standards Used by Hard Drives (7 of 11)
Figure 5-12 A SATA data cable and SATA power cable

## Slide 19: Interface Standards Used by Hard Drives (8 of 11)
The SATA 3.2 revision allows for PCIe and SATA to work together in a technology called SATA Express
  Uses a new connector
  SATA Express is not as fast as NVMe
A motherboard or expansion card can provide external SATA (eSATA) ports for external drives
External SATA (eSATA)
  eSATA drives use a special external shielded serial ATA cable up to 2 meters long
Purchasing considerations
  SATA standards for the drive and motherboard need to match
  If they do not match, the system runs at the slower speed

## Slide 20: Interface Standards Used by Hard Drives (9 of 11)
NVMe
  NVMe (Non-Volatile Memory Express or NVM Express) interface standard is used only by SSDs
  Comparisons:
    The most common SATA standard, SATA 3, transfers data at 6 Gb/sec
    NVMe uses the most common PCIe standard, PCIe 3.0, which transfers data at 32 Gb/sec
  The PCIe NVMe interface might be used in three ways:
    PCIe expansion card
    U.2 slot
    M.2 port

## Slide 21: Interface Standards Used by Hard Drives (10 of 11)
Figure 5-16 A U.2 2.5” SSD uses the NVMe and PCIe interface standards and connects to a U.2 port on the motherboard

## Slide 22: Interface Standards Used by Hard Drives (11 of 11)
Figure 5-18 Install up to four M.2 SSDs in a bootable RAID array on this adapter card by Asus

## Slide 23: How to Select and Install Hard Drives
Topics covered in this part of the chapter:
  Selecting a hard drive
  Installation details for a SATA drive
  How to install a hard drive in a bay too wide for the drive
  Special considerations to install a hard drive in a laptop
  How to set up a RAID system

## Slide 24: Selecting a Hard Drive (1 of 3)
The motherboard and hard drive must support the same interface standard
  Find out by reading the motherboard manual
Options for compatibility:
  SATA ports on a motherboard are usually color-coded to indicate which SATA standard the port supports
  M.2 slots might support PCIe 3.0, PCIe 2.0, SATA2, SATA3, or USB 3.0
  When an M.2 port with a card installed is using the SATA bus, one of the SATA ports might be disabled
  NVMe expansion cards most likely use a PCIe x4 version 3.0 slot

## Slide 25: Selecting a Hard Drive (2 of 3)
Considerations when selecting a hard drive:
  Technology
  Form factor
  Capacity
  Data transfer rate as determined by the drive interface
  For magnetic drives, the spindle speed, which affects performance
  For hybrid drives, the cache or buffer size, which affects performance

## Slide 26: Selecting a Hard Drive (3 of 3)
Manufacturer | Website
Kingston Technology (SSD only) | kingston.com
Samsung (SSD only) | samsung.com
Seagate Technology (magnetic and SSD) | seagate.com
Western Digital (magnetic and SSD) | wdc.com
Toshiba (magnetic and SSD) | Toshiba.com

## Slide 27: Steps to Install a SATA Drive (1 of 8)
A SATA drive might have jumpers
  Most likely set by factory as they should be
Some SATA drives have two power connectors
  Choose only one to use
  Never install two power cords at the same time

## Slide 28: Steps to Install a SATA Drive (2 of 8)
Figure 5-19 The rear of a SATA drive

## Slide 29: Steps to Install a SATA Drive (3 of 8)
Step 1: As Best You Can, Protect the User’s Data
  Back up important data to other media and verify that you can access the data on that media
Step 2: Know Your Starting Point
  How is your system configured?
  Is everything working properly?
  Write down what you know about the system
Step 3: Read the Documentation and Prepare Your Work Area
  Read all installation instructions first
  Visualize all the steps in the installation
  Protect against ESD and avoid working on carpet

## Slide 30: Steps to Install a SATA Drive (4 of 8)
Step 3: Read the Documentation and Prepare Your Work Area (continued)
  Added precautions:
    Handle the drive carefully
    Do not touch any exposed circuitry
    Prevent other people from touching exposed microchips
    Drain static electricity from the package and from your body by touching metal for at least 2 seconds
    If you must set it down, place it component-side up
    Do not place the drive on the computer case or on a metal table

## Slide 31: Steps to Install a SATA Drive (5 of 8)
Step 4: Install the Drive
  Shut down the computer and unplug it
  Decide which bay will hold the drive
  Slide drive in the bay and secure it (use two screws on both sides)
  Use correct motherboard SATA connector
  Connect a 15-pin SATA or 4-pin Molex power connector from the power supply to the drive
  Check all connections and power up the system
  Verify the drive is recognized correctly via BIOS/UEFI setup

## Slide 32: Steps to Install a SATA Drive (6 of 8)
Figure 5-26 Connect the SATA power cord to the drive

## Slide 33: Steps to Install a SATA Drive (7 of 8)
Figure 5-27 A BIOS/UEFI setup screen showing a SATA hard drive and DVD drive installed

## Slide 34: Steps to Install a SATA Drive (8 of 8)
You are ready to prepare the hard drive for first use
  Boot from Windows setup DVD
    Follow directions on the screen to install Windows on the new drive
  If installing a second hard drive with Windows installed on the first drive use Windows Disk Management utility to partition and format the second drive

## Slide 35: Installing a Drive in a Removable Bay
Unplug the cage fan from its power source
Turn handle on each locking device counterclockwise to remove it
Slide the bay to the front and out of the case
Insert hard drive in the bay
  Use two screws on each side to anchor the drive in the bay
Slide the bay back into the case
Reinstall the locking pins
Plug in the cage fan power cord

## Slide 36: Installing a Small Drive in a Wide Bay (1 of 2)
Use a universal bay kit to securely fit a small drive into the bay
The adapter spans the distance between the sides of the drive and bay

## Slide 37: Installing a Small Drive in a Wide Bay (2 of 2)
Figure 5-30 Use the universal bay kit to make the drive fit the bay

## Slide 38: Installing an M.2 SSD Card
Read the motherboard manual to find out the types of M.2 cards the board supports
Do the following to install the card:
  1. Measure the length of the card and decide which screw hole for the M.2 slot the card requires
    Install standoff in hole
  2. Slide the card straight into the slot, but not from an upward angle
  3. Install the one screw in the standoff to secure the card to the motherboard
  4. Start the system, go into BIOS/UEFI setup, and make sure the M.2 card is recognized by the system

## Slide 39: Installing a Hard Drive in a Laptop (1 of 2)
General guidelines:
  See manufacturer’s documentation for drive sizes, form factors, and connector types
  Be aware of voiding manufacturer’s warranty
  If the old drive has crashed, you’ll need the recovery media to reinstall Windows and the drivers
  If you are upgrading from a low-capacity drive to a higher-capacity drive, you need to consider how you will transfer data from the old drive to the new one
Considerations when shopping for a laptop drive:
  Laptop drive is 2.5 or 1.8 inches wide
    Some high-end laptops use an M.2 SSD
  For a 2.5” drive, expect it to use the SATA interface

## Slide 40: Installing a Hard Drive in a Laptop (2 of 2)
Older laptop computers required disassembly
Newer laptops should be easy to replace
  Power down system, remove peripherals, and remove the battery pack
  Remove a screw that holds the drive in place
  Open the lid of the laptop slightly
  Turn the laptop on its side and push the drive out of its bay
  Remove the plastic cover from the drive and move the cover to the new drive
  Insert the new drive in the bay, replace the screw, and power up the system
  BIOS/UEFI should recognize the new drive and search for an OS
  If drive is new, boot from the Windows setup or recovery DVD and install the OS

## Slide 41: Setting Up Hardware RAID
RAID (Redundant Array of Inexpensive Disks)
  Also called: Redundant Array of Independent Disks
  A technology that configures two or more hard drives to work together as an array of drives
Why use RAID?
  To improve performance by writing data to two or more hard drives to that a single drive is not excessively used
  To improve fault tolerance by writing two copies of it, each to a different hard drive

## Slide 42: Types of RAID (1 of 3)
Spanning: sometimes called JBOD (just a bunch of disks)
  Uses two hard drives to hold a single Windows volume
  When one drive is full, data is written to second drive
RAID 0: uses two or more physical disks
  Writes to physical disks evenly across all disks so that no one disk receives all activity
  Windows calls RAID 0 a striped volume
RAID 1: Mirroring (mirrored volume)
  Duplicates data on one drive to another drive and is used for fault tolerance
RAID 5: uses three or more drives
  Stripes data across drives and uses parity checking and data is not duplicated
RAID 10: RAID 1+0 (pronounced RAID one zero)
  Combination of RAID 1 and RAID 0
  Takes at least 4 disks and data is mirrored across pairs of disks

## Slide 43: Types of RAID (2 of 3)
Figure 5-36 Ways that hard drives can work together

## Slide 44: Types of RAID (3 of 3)
Figure 5-37 RAID 1 and RAID 10

## Slide 45: How to Implement Hardware RAID (1 of 4)
Hardware RAID can be set up by using:
  A RAID-enabled motherboard that is managed in BIOS/UEFI setup
  A RAID controller card
For best RAID performance:
  All hard drives in an array should be identical in brand, size, speed, other features
If Windows is to be installed on a RAID hard drive
  RAID must be implemented before Windows is installed

## Slide 46: How to Implement Hardware RAID (2 of 4)
General directions to install a RAID 5 array using three matching SATA drives
  Install drives in the computer case and connect each drive to motherboard
  Boot system and enter BIOS/UEFI setup
    Verify drives are recognized, select option to configure SATA, and select RAID
  Reboot the system
    Press <Ctrl+I> to enter the RAID configuration utility
  Select option 1 to “Create RAID Volume”
  Under RAID Level, select RAID 5 (Parity) and Strip Size value
  Enter the size of the volume
  Select Create Volume to complete the RAID configuration

## Slide 47: How to Implement Hardware RAID (3 of 4)
Figure 5-40 Use a BIOS/UEFI utility to configure a RAID array

## Slide 48: How to Implement Hardware RAID (4 of 4)
Figure 5-41 Make your choices for the RAID array

## Slide 49: NAS Devices and External Storage (1 of 2)
Hard drives are sometimes stored in external enclosures
  Make it easy to expand storage capacity of a single computer or make available hard drive storage to an entire network
For network attached storage (NAS)
  The enclosure connects to the network via an Ethernet port
Hard drives inside the enclosure might use a SATA connection

## Slide 50: NAS Devices and External Storage (2 of 2)
What to know about supporting external enclosures:
  An enclosure might contain firmware that supports RAID
  To replace a hard drive in an enclosure, see the documentation for the enclosure
  If a computer case is overheating, remove hard drives from the case and install them in an external enclosure
    It is better to leave the hard drive that contains the Windows installation in the case
  You can purchase a SATA controller card that provides external eSATA connectors to be used when:
    The motherboard eSATA port is not functioning
    The motherboard does not support a fast SATA standard that your hard drives use

## Slide 51: Supporting Other Types of Storage Devices
This section covers:
  File systems that other types of storage devices use
  The following types of storage devices:
    Optical discs
    USB flash drives
    Memory cards

## Slide 52: File Systems Used By Storage Devices (1 of 2)
File system – used to manage data stored on a device
  Overall structure the OS uses to name, store, and organize files on a drive
  In Windows, each storage device or group of devices (RAID) is assigned a driver letter and is called a volume
Formatting – installing a new file system on a device
Types of file systems:
  NTFS
  exFAT
  FAT32 and FAT
  CDFS (Compact Disc File System) or UDF (Universal Disk Format)
  A newer version of UDF is used by DVDs and BDs (Blu-ray discs)

## Slide 53: File Systems Used By Storage Devices (2 of 2)
Figure 5-44 This 16-GB USB flash drive is using the FAT32 file system

## Slide 54: Standards Used By Optical Discs and Drives (1 of 4)
CDs (compact discs), DVDs (digital versatile discs or digital video discs), and BDs (Blu-ray discs) use similar laser technologies
  Tiny lands and pits on surface represent bits read by a laser beam
Optical Discs:
  Data can be written to:
    One side of a CD
    One or both sides of a DVD or Blu-ray disc
  DVD or Blu-ray disc can hold data in two layers on each side

## Slide 55: Standards Used By Optical Discs and Drives (2 of 4)
Figure 5-47 Storage capacities for CDs, DVDs, and BDs

## Slide 56: Standards Used By Optical Discs and Drives (3 of 4)
Optical Drives and Burners:
  Blu-ray drives are backward compatible with DVD and CD technologies
  DVD drives are backward compatible with CD technologies
  Depending on the drive features, an optical drive might be able to read and write to BDs, DVDs, and CDs
  A drive that can write to discs is commonly called a burner
  Today’s internal optical drives interface with the motherboard via a SATA connection
  An external drive might use an eSATA or USB port

## Slide 57: Standards Used By Optical Discs and Drives (4 of 4)
Figure 5-49 The PX-610U external DVD±RW drive by Plextor uses a USB 2.0 port

## Slide 58: Installing an Optical Drive
Internal optical drives on today’s computer use a SATA interface
An optical drive is usually installed in the drive bay at the top of a desktop case
  After installed in the bay, connect the data and power cables
Windows 10/8/7 supports optical drives using its own embedded drives without add-on drivers

## Slide 59: Replacing an Optical Drive on a Laptop (1 of 2)
For some systems, you will need to first remove the keyboard to expose an optical drive
Replacing optical drives:
  Shut down the system, unplug the AC adapter, and remove the battery pack
  Remove the keyboard (not all laptops require this step)
  Remove the screw holding DVD drive to the laptop
  Slide drive out of the bay and new drive into the bay
    Ensure connection with drive connector at the back of the bay
    Replace the screw

## Slide 60: Replacing an Optical Drive on a Laptop (2 of 2)
Figure 5-53 Remove the keyboard to expose the optical drive.

## Slide 61: Solid-State Storage (1 of 3)
Solid-state storage includes:
  SSDs, USB flash drives, and memory cards
USB flash drives go by many names:
  Flash pen drive, jump drive, thumb drive, and key drive
  Flash drives might work at USB 2.0 or USB 3.0 speed and use FAT or exFAT file system
  Windows 10/8/7 has embedded drivers to support flash drives
Memory cards might be used in:
  Digital cameras, tablets, smartphones, MP3 players, digital camcorders, etc…
  Most laptops have memory card slots provided by a built-in smart card reader

## Slide 62: Solid-State Storage (2 of 3)
Secure Digital (SD) cards are the most popular memory cards
Three standards for capacity used by SD cards:
  1.x (regular SD)
  2.x (SD High Capacity or SDHC)
  3.x (SD eXtended Capacity or SDXC)
SD cards come in three physical sizes: full-size, MiniSD, and MicroSD
SDHC and SDXC slots are backward compatible with SD cards
Cannot use:
  An SDHC card in an SD slot
  An SDXC card in an SDHC or SD slot
SD and SDHC cards use FAT file system
SDXC cards use exFAT file system

## Slide 63: Solid-State Storage (3 of 3)
Figure 5-60 Flash memory cards

## Slide 64: Troubleshooting Hard Drives
Problems caused by hard drive during the boot can be caused by:
  Hard drive subsystem
  File system on the drive
  Files required by Windows when it begins to load
When trying to solve a problem with the boot
  Decide if the problem is caused by hardware or software

## Slide 65: Slow Performance (1 of 2)
One of the most common complaints:
  Computer is running slowly
The overall performance of a system depends on the individual performances of:
  The processor, motherboard, memory, and hard drive
To optimize a drive:
  You can use Windows tools or tools provided by the hard drive manufacturer
Use the Windows Defrag and Optimization tool (dfrgui.exe) to verify that Windows is defragmenting a magnetic drive and trimming an SSD

## Slide 66: Slow Performance (2 of 2)
Figure 5-61 Windows reports volume C: is trimmed and volume D: is not fragmented

## Slide 67: Hard Drive Problems During the Boot (1 of 4)
Hardware problems usually show up at POST
If BIOS/UEFI cannot access the drive, the cause might be due to the drive, data cable, electrical system, motherboard, or a loose connection
Things to do and check before opening case:
  Check to see if BIOS/UEFI displays a numeric error code or other message during POST
  Check BIOS/UEFI setup for errors in the hard drive configuration
  Try booting from another bootable media
  For a RAID array, use the firmware utility to check the status of each disk in the array and check for errors

## Slide 68: Hard Drive Problems During the Boot (2 of 4)
If the problem is still not solved, open case and check these things:
  Remove and reattach all drive cables
  If using a RAID or SATA controller card, remove and reseat it or place in a different slot
  Inspect drive for damage
  Determine if hard drive is spinning by listening to it
  Check the cable for frayed edges
  Check installation manual
  S.M.A.R.T. errors mean data should be backed up and drive replaced as soon as possible
  Use Windows tools for checking a hard drive
    Windows 10/8/7 Startup Repair
    chkdsk command

## Slide 69: Hard Drive Problems During the Boot (3 of 4)
If the problem is still not solved, open case and check these things (continued):
  Steps to take to repair an MBR hard drive:
    Repair the BCD using bootrec /RebuildBCD
    Repair the boot sector using bootrec /FixBoot
    Repair the MBR using bootrec /FixMBR
  Check the drive manufacturer’s web site for diagnostic software
  Move the device to a working computer and install it as a second drive
  Try these things to clean the drive and get a fresh start:
    Format a hard drive volume
    Use diskpart to start over with a fresh file system

## Slide 70: Hard Drive Problems During the Boot (4 of 4)
If the problem is still not solved, open case and check these things (continued):
  Exchange the three field replaceable units-the data cable, the storage card, and the hard drive
    Try connecting the drive data cable to a different SATA connector
    Reconnect or swap the drive data cable
    Reseat or exchange the drive controller card
    Exchange the hard drive for a known good drive
  If your drive whines loudly, try replacing it
  A bad power supply or a bad motherboard also might cause a disk boot failure

## Slide 71: Chapter Summary (1 of 3)
A hard disk drive (HDD) can be magnetic, solid-state, or hybrid
A solid-state drive contains NAND flash memory and is more expensive, faster, more reliable, and uses less power than a magnetic drive
A hybrid hard drive (H-HDD) is a magnetic drive with an SSD buffer that improves performance
S.M.A.R.T is a self-monitoring technology whereby the BIOS/UEFI monitors the health of a hard drive
Three SATA standards provide data rates of 1.5 Gb/sec, 3.0 Gb/sec, and 16.0 Gb/sec
When selecting a hard drive, consider the interface standards, storage capacity, technology, spindle speed, interface standard, and buffer size

## Slide 72: Chapter Summary (2 of 3)
SATA drives require no configuration and are installed using a power cord and a data cable
Laptop hard drives plug directly into a SATA connection on the system board
RAID technology uses an array of hard drives to provide fault tolerance and/or improvement in performance
Hardware RAID is implemented using the motherboard BIOS/UEFI or a RAID controller card
Software RAID is implemented in Windows
Multiple hard drives can be installed in a single external enclosure to expand the storage capacity of a single computer or to make hard drive storage available on a network as network attached storage (NAS)
File systems a storage device might use in Windows include NTFS, exFAT, FAT32, FAT, CDFS, and UDF
Optical discs can be recordable (CD-R) or rewritable (DVD-RW)

## Slide 73: Chapter Summary (3 of 3)
Flash memory cards are a type of solid-state storage
Defragmenting a magnetic hard drive can sometimes improve slow performance of the drives
Hard drive problems during the boot can be caused by the hard drive subsystem, the file system on the drive, or files required by Windows when it begins to load
To determine if the hard drive is the problem when booting, try to boot from other media
For problems with a RAID volume, use the RAID controller firmware or RAID management software in Windows to report the status of the array and to rebuild the RAID volume
To determine if a drive has bad sectors, use the chkdsk command
Use commands within the diskpart utility to completely erase a partition on a hard drive
Field replaceable units in the hard drive subsystem are the data cable, optional storage card, and hard drive