## Slide 1: CompTIA A+ Guide to IT Technical Support
10th Edition

## Slide 2: Supporting I/O Devices
Chapter 6

## Slide 3: Objectives
Describe the general approach technicians use to install and support I/O devices
Install and configure several I/O devices, such as barcode readers, biometric devices, pay devices, webcams, graphic tablets, signature pads, and touch screens
Install and configure adapter cards
Support the video subsystem, including selecting a monitor and video card and supporting dual monitors
Troubleshoot common problems with I/O devices
Customize a computer system to meet customer needs

## Slide 4: Basic Principles for Supporting Devices
I/O or storage devices may be internal or external
Basic principles apply to both internal and external devices:
  Every device is controlled by software
  Best guide for installation and support is the manufacturer
  Some devices need application software to use with the device
  A device is no faster than the port/slot it is designed to use
  Use an administrator account in Windows
  Problems are sometimes solved by updating drivers or firmware
  Install only one device at a time
Device Manager (devmgmt.msc):
  Primary Windows tool for managing hardware
Using Device Manager you can:
  Disable or enable a device, update its drivers, uninstall a device, undo a driver update

## Slide 5: Wired and Wireless Connection Standards Used by Peripheral Devices (1 of 2)
Port or Wireless Type | Maximum Speed | Maximum Cable Length or Wireless Range
Thunderbolt 3 | 40 Gbps | Copper cables up to 2 meters; requires USB-C connector
Thunderbolt 2 | 20 Gbps | Copper cables up to 100 meters
SuperSpeed+ USB (USB 3.2) | 20 Gbps | For maximum speed, cable length up to 1 meter; requires USB-C connector
SuperSpeed+ USB (USB 3.1) | 10 Gbps | Cable lengths up to 3 meters
eSATA Version 3 (eSATA-600) | 6.0 Gbps | Cable lengths up to 2 meters
SuperSpeed USB (USB 3.0) | 5.0 Gbps | Cable lengths up to 3 meters
eSATA Version 2 (eSATA-300) | 3.0 Gbps | Cable lengths up to 2 meters
eSATA Version 1 (eSATA-150) | 1.5 Gbps or 1500 Mbps | Cable lengths up to 2 meters
Wi-Fi 802.11ac RF of 5.0 GHz | 1.3 Gbps or 1300 Mbps | Range up to 70 meters

## Slide 6: Wired and Wireless Connection Standards Used by Peripheral Devices (2 of 2)
Port or Wireless Type | Maximum Speed | Maximum Cable Length or Wireless Range
Wi-Fi 802.11n | Up to 600 Mbps | Range up to 70 meters
Lightning | 480 Mbps | Cable lengths up to 2 meters
Hi-Speed USB (USB 2.0) | 480 Mbps | Cable lengths up to 5 meters
Original USB (USB 1.1) | 12 Mbps or 1.2 Mbps | Cable lengths up to 3 meters
Wi-Fi 802.11g RF of 2.4 GHz | Up to 54 Mbps | Range up to 100 meters
Wi-Fi 802.11a RF of 5.0 GHz | Up to 54 Mbps | Range up to 50 meters
Wi-Fi 802.11b RF of 2.4 GHz | Up to 11 Mbps | Range up to 100 meters
Bluetooth wireless RF of 2.45 GHz | Up to 3 Mbps | Range up to 10 meters
Near Field Communication (NFC) RF of 13.56 MHz | Up to 424 kbps | Range up to 4 centimeters

## Slide 7: Connectors and Ports Used by Peripheral Devices (1 of 8)
USB Connections and Ports
  As many as 127 USB devices can be daisy chained together
  USB uses serial transmissions and devices are hot-swappable (plug and unplug without powering down)
  A USB cable has four wires, two for power and two for communication

## Slide 8: Connectors and Ports Used by Peripheral Devices (2 of 8)
Figure 6-1 SuperSpeed+, SuperSpeed, Hi-Speed, and Original USB logos appear on products certified by the USB Forum

## Slide 9: Connectors and Ports Used by Peripheral Devices (3 of 8)
Video Connectors and Ports
  Video ports are provided by a video card or the motherboard
  Video cards are sometimes called:
    Graphic adapters, graphics cards, or display cards
  Most motherboards sold today have one or more onboard video ports
  Types of video ports:
    VGA
    DVI
    DisplayPort
    HDMI and HDMI mini

## Slide 10: Connectors and Ports Used by Peripheral Devices (4 of 8)
Figure 6-3 Two types of DVI ports: (A) DVI-D, (B) DVI-I

## Slide 11: Connectors and Ports Used by Peripheral Devices (5 of 8)
Figure 6-5 A DisplayPort to Mini DisplayPort cable

## Slide 12: Connectors and Ports Used by Peripheral Devices (6 of 8)
Figure 6-6 Use BIOS/UEFI setup to enable or disable onboard ports

## Slide 13: Connectors and Ports Used by Peripheral Devices (7 of 8)
Figure 6-7 An HDMI to mini-HDMI cable

## Slide 14: Connectors and Ports Used by Peripheral Devices (8 of 8)
Additional Connectors and Ports
  Thunderbolt is a multipurpose connector used for high-end displays, external storage devices, and to charge power for smartphones and laptops
  eSATA port is used for connecting external storage devices to a computer
  Lightning connector is an Apple-specific connector for its mobile devices
  BNC, RG-6, and RG-50
    Connectors for coaxial cable
  RS-232 connectors have been replaced primarily by USB or other connectors

## Slide 15: Identifying and Installing I/O Peripheral Devices
Simple input devices (mouse and keyboard) can be controlled by the BIOS/UEFI or have embedded drivers built into the OS
General procedures to install any peripheral device:
  1. Read the manufacturer’s directions
  2. Make sure the drivers are written for the proper OS
  3. Make sure the motherboard port you are using is enabled
  4. Install drivers or plug in the device
  5. Install the application software to use the device

## Slide 16: Mouse or Keyboard (1 of 4)
Plug a mouse or keyboard into a USB and Windows should automatically recognize it and install generic drivers
  Older PS/2 ports are not hot-pluggable, so you must restart Windows after plugging into this type of port
For keyboards with special features:
    Install drivers that came with the keyboard
Use Device Manager to uninstall, disable, or enable most devices
    USB devices are managed through Programs and Features window

## Slide 17: Mouse or Keyboard (2 of 4)
Figure 6-17 USB devices are listed as installed programs

## Slide 18: Mouse or Keyboard (3 of 4)
Replace the Keyboard and Touch Pad in a Laptop
  Power down the laptop and remove AC adapter and battery pack
  Remove screws on bottom of laptop
  Turn the laptop over and open lid
    Push keyboard toward lid while pulling it up to release it from the case
  Bring keyboard out of the case and forward
    Expose keyboard ribbon cable
    Use spudger or tweezers to lift cable connector up and out
  Replace keyboard following steps in reverse order
  If touchpad is part of keyboard bezel, remove keyboard before removing the keyboard bezel

## Slide 19: Mouse or Keyboard (4 of 4)
Figure 6-20 Disconnect the keyboard cable from the motherboard

## Slide 20: Barcode Readers
Barcode readers are used to scan barcodes on products at point of sale (POS)
Several interface methods:
  Wireless connection, serial port, USB port, or keyboard port
If the reader uses a keyboard port:
  It most likely contains a splitter (keyboard wedge) for the keyboard to use, and data read by the barcode reader is input into the system

## Slide 21: Pay Devices
A magnetic stripe reader and chip reader can read from the stripe or chip to pull information from a card or license
  Sends information to the computer through a serial connection, USB connection, Lightning connection, 3.5-mm headphone jack, or a stripe reader wedge mounted on a keyboard
A tap pay device connects wirelessly or by cable to a computer or mobile device to turn it into a point-of-sale system

## Slide 22: Signature Pads
A signature pad uses a sensitive touch screen to capture a handwritten signature made using a stylus or finger for a receipt, contract, or ID card
The signature pad LCD panel displays electronic ink
Signature pads typically use a serial or USB connection and include software installed on the computer to process the signature

## Slide 23: Biometric Devices (1 of 2)
A biometric device inputs biological data about a person to identify the person’s fingerprint, handprint, face, voice, eye, or handwritten signature
Fingerprint readers may:
  Look like a mouse
  Use wireless or USB connection
  Be embedded on the side of a keyboard, flash drive or laptop
Read documentation to know if you should install drivers before plugging in device

## Slide 24: Biometric Devices (2 of 2)
Figure 6-25 Fingerprint readers can (A) look like a mouse, or (B) be embedded on a keyboard

## Slide 25: Webcams (1 of 2)
A webcam (web camera):
  Is embedded on most laptops
  Can be installed using a USB port or other port
  Comes with built-in microphone
    Use this microphone or use the microphone port on the computer
  Use the setup CD to install the software and then plug in the webcam to a USB port

## Slide 26: Webcams (2 of 2)
Figure 6-27 The Camtasia Recorder application allows you to change the input devices used for video and sound

## Slide 27: Graphics Tablets
A graphics tablet (also called digitizing tablet) is used to hand draw
  Likely to connect by a USB port
  Comes with stylus that works like a pencil
  A graphics tablet and stylus can be a replacement for a mouse or touch pad
  Popular with graphic artists and others who use desktop publishing applications
  Install the same way as other USB devices

## Slide 28: Touch Screens
A touch screen is an input device that uses a monitor or LCD panel as the backdrop for input options
  Some laptops and monitors for desktops have built-in touch screens
  Can be installed as an add-on
  For most installations, install drivers before connecting by way of a USB port
  Use management software that came with the device to control and calibrate

## Slide 29: Virtual Reality Headsets
A VR (virtual reality) headset is a device worn on the head that creates a visual and audible virtual experience for the user using a lens display, speakers, microphone, and head-tracking sensors for interaction
  Often used for extreme gaming and military training
VR headsets can be programmed independently of a computer
  Or the headset can be connected to a computer using USB for more programming input or recording the experience
Some VR headsets include a dock for a smartphone

## Slide 30: KVM Switches
A KVM (Keyboard, Video, and Mouse) switch allows the use of one keyboard, mouse, and monitor for multiple computers
  Useful in a server room or testing lab
  Does not require device drivers, just plug in cables form each computer to the device
  Switch between computers by using a hot key on the keyboard, buttons on KVM switch, or a wired remote

## Slide 31: Installing and Configuring Adapter Cards (1 of 3)
When preparing to install an adapter card:
  Verify that the card fits an empty expansion slot
  Verify that the device drivers for the OS are available
  Back up important data not already backed up
  Know your starting point
General directions to install an adapter card
  Read the documentation for the card
  If replacing an onboard port, disable port in BIOS/UEFI setup
  Wear ESD strap, shut down system, unplug power cords and cables, and drain power
  Locate slot and prepare for installation

## Slide 32: Installing and Configuring Adapter Cards (2 of 3)
General directions to install an adapter card (continued)
  Insert card into expansion slot
  Anchor card to top of the slot with screws
  Connect any power cords or data cables
  Replace the case cover, plug in any essential peripherals
  Start the system – Windows should detect a new hardware device and attempt to automatically install the drivers
  If a CD came with the device, insert and run the setup program
  You may have to restart the system
    If there are any problems with installation, turn to Device Manager to troubleshoot

## Slide 33: Installing and Configuring Adapter Cards (3 of 3)
Figure 6-35 An opening menu to install video drivers

## Slide 34: Sound Cards and Onboard Sound (1 of 2)
A sound card or onboard sound can play and record sound and save it in a file
Color-coded speaker ports are for speakers and subwoofer
Ports may also be available to connect to external sound equipment such as a CD or DVD player

## Slide 35: Sound Cards and Onboard Sound (2 of 2)
Figure 6-36 The Sound Blaster X-Fi Titanium sound card by Creative uses a PCIe x1 slot

## Slide 36: Replacing Expansion Cards in a Laptop (1 of 3)
Newer laptops are likely to use Mini PCI Express slots (Mini PCIe)
  Uses 52 pins on the edge connector
Older notebooks use a Mini PCI slot
For many laptops, remove a cover on the bottom of the laptop to expose expansion cards
  For cards that have an antenna, be sure to remove the antenna wires before replacing card
Use Device Manager to ensure the device is working properly after install

## Slide 37: Replacing Expansion Cards in a Laptop (2 of 3)
Figure 6-38 Removing the cover from the bottom of a laptop exposes several internal components

## Slide 38: Replacing Expansion Cards in a Laptop (3 of 3)
Figure 6-40 How to remove a Mini PCI Express card

## Slide 39: Supporting the Video Subsystem
A monitor is the primary output device of a computer
Two necessary components for video output:
  Monitor
  Video card (also called video adapter or graphics card) or video port on motherboard

## Slide 40: Monitor Technologies and Features (1 of 5)
Types of monitors:
  LCD (liquid crystal display) - also called a flat-panel monitor
    First used in laptops
    At the center of layers is liquid crystal material
    Layers are sandwiched between two grids of electrodes forming columns and rows
    Each intersection of row and column forms a pixel
  OLED (organic light-emitting Diode) monitor uses a thin LED (light-emitting diode) layer or film between two grids of electrodes and does not use backlighting
    Does not emit as much light as an LCD monitor, therefore, can produce deeper blacks, provide better contrast, work in darker rooms, and use less power than an LCD monitor
    Projector – used to shine a light that projects a transparent image onto a large screen

## Slide 41: Monitor Technologies and Features (2 of 5)
Figure 6-42 Layers of an LCD panel

## Slide 42: Monitor Technologies and Features (3 of 5)
Figure 6-43 A portable XGA projector by Panasonic

## Slide 43: Monitor Technologies and Features (4 of 5)
Monitor Characteristic | Description
Screen size | The screen size is the diagonal length of the screen surface in inches.
Refresh rate | The refresh rate is the number of times a monitor screen is built or refreshed in 1 second, measured in Hz (cycles per second).
Pixel pitch | A pixel is a spot or dot on the screen that can be addressed by software. The pixel pitch is the distance between adjacent pixels on the screen-the smaller the number, the better.
Resolution | The resolution is the number of spots or pixels on a screen that can be addressed by software.
Contrast ratio | Contrast ratio is the contrast between true black and true white on the screen-the higher the contrast ratio, the better.
Viewing angle | The viewing angle is the angle at which a monitor becomes difficult to see from the side.
Backlighting or brightness | Brightness is measured in cd/m2 , which is the same as lumens/m2 .
Connectors | Popular options for connectors are VGA, DVI-I, DVI-D, HDMI, DisplayPort, and Apple’s Thunderbolt.
Other features | LCD monitors can also provide a privacy or antiglare surface, tilt screens, microphone input, speakers, USB ports, adjustable stands, and perhaps even an input for your smartphone.

## Slide 44: Monitor Technologies and Features (5 of 5)
Figure 6-45 The rear of this LCD monitor shows digital and analog video ports to accommodate a video cable with either a 15-pin analog VGA connector or a digital DVI connector

## Slide 45: Changing Monitor Settings
Settings that apply to the monitor can be managed by using the monitor buttons, function keys on a keyboard, and Windows utilities
Using the monitor buttons, you can:
  Adjust horizontal and vertical position of the screen
  Change the brightness and contrast settings
On laptops, function keys are usually used instead of buttons
Windows utilities can also be used to change monitor settings

## Slide 46: Troubleshooting I/O Devices
When troubleshooting peripheral devices:
  Always try the least invasive and least expensive solutions first
This section covers how to handle some of the errors or problems you might encounter

## Slide 47: NumLock Indicator Light
When users complain that they cannot sign in to Windows even when entering the correct password:
  Have them make sure the NumLock key is set correctly
  Laptops use this key to toggle between the keys interpreted as letters and numbers
  Most laptops have a NumLock indicator light near the keyboard

## Slide 48: Device Manager (1 of 2)
Device Manager is usually a good place to start troubleshooting
To see a device’s properties box, right-click the device and click Properties
Try updating the drivers
  Click Update Driver on the General tab or Driver tab
  If driver update creates a problem, roll back (undo) the driver update if the previous drivers were working
Try to uninstall the device and reinstall it
  Click Uninstall on the Driver tab

## Slide 49: Device Manager (2 of 2)
Update Port or Slot Drivers on a Laptop
  If you have a problem with a port or slot on a laptop, use Device Manager to see if errors are reported
    Also you can update drivers for the port or slot
  Manufacturers often store backups of the drivers on the hard drive under support tools
    And on the recovery media, if available
  Download the latest drivers from the manufacturer’s website
  Still not solved, use Device Manager to uninstall the port or slot drivers and use support tools to reinstall

## Slide 50: Troubleshooting Video, Monitors, and Projectors (1 of 9)
For monitor and video problems, try easy things first such as:
  Check cable connections and check contrast/brightness adjustments
Problems With Video Card Installations
  When you first power up the system, you hear a whining sound
    Caused by card not getting enough power (power supply might be inadequate)
  When you first start the system, you see nothing but a black screen
    Most likely caused by the onboard video port not being disabled in BIOS/UEFI setup
  When you first start up the system, you hear a series of beeps
    UEFI/BIOS cannot detect video card (try reseating)
  Error messages about video appear when Windows starts
    May be a conflict with onboard video port (disable port)
  Games crash or lock up
    Try updating the drivers for the motherboard, video card, and the sound card

## Slide 51: Troubleshooting Video, Monitors, and Projectors (2 of 9)
Monitor Indicator Light Is Not On; No Image On Screen
  Ask these questions and try these things:
    Is the monitor power cable plugged in?
    Is the monitor turned on?
    Is the monitor cable plugged into the video port at the back of the PC?
    Try a different monitor and a different monitor cable

## Slide 52: Troubleshooting Video, Monitors, and Projectors (3 of 9)
Monitor Indicator Light Is On; No Image On Screen
  Try these things:
    Ensure video cable is securely connected
    If monitor displays POST but goes blank when Windows starts to load:
      Problem is with Windows, not the monitor
    Ensure monitor is set to correct voltage (110 vs. 220)
    Might be a problem with video card
    Verify video cable connection inside case
    Check the contrast adjustment
    Check brightness or backlight adjustment

## Slide 53: Troubleshooting Video, Monitors, and Projectors (4 of 9)
Monitor Indicator Light Is On; No Image On Screen (continued)
  Try these things:
    Switch out monitor-to-computer cable
    Test a monitor you know is good on the computer you suspect is bad
    Check for loose socketed chips on the card
    Reseat the video card
    Trade a good video for suspected bad video card
    Test the RAM on the motherboard
    Try using a backup PCI video card if using a PCI-Express card
    Trade the motherboard for one you know is good

## Slide 54: Troubleshooting Video, Monitors, and Projectors (5 of 9)
Screen Goes Blank 30 Seconds or One Minute After the Keyboard Is Left Untouched
  If keyboard is a Green motherboard and is being used with an Energy Saver monitor
    Monitor can be configured to go into standby or sleep mode after a period of inactivity
    This feature can also help prevent burn-in (a permanent impression of an image is left on monitor)
  Use the Power Options applet in Control Panel to configure the sleep settings on a computer

## Slide 55: Troubleshooting Video, Monitors, and Projectors (6 of 9)
Poor Display
  Solve these problems by using controls on the monitor and Windows settings - Do the following:
    LCD monitor controls – usually located on front of monitor
    Windows display settings – use to adjust font size, screen resolution, brightness, color, and Clear Type text
    Update video drivers
    Dead pixels – pixels that are not working
    Dim image – laptops dim the LCD screen when the computer is running on battery
      Brighten the screen using the Windows display settings
    Artifacts – horizontally torn images on-screen
      Try updating video drivers
      Overclocking can cause artifacts
  Poor display might be caused by inadequate video RAM

## Slide 56: Troubleshooting Video, Monitors, and Projectors (7 of 9)
Figure 6-51 Two screens in the Windows 10 color calibration wizard (A)

## Slide 57: Troubleshooting Video, Monitors, and Projectors (8 of 9)
Figure 6-51 Two screens in the Windows 10 color calibration wizard (B)

## Slide 58: Troubleshooting Video, Monitors, and Projectors (9 of 9)
Cannot Connect To External Monitor or Projector
  Try the following solutions:
    Make sure the monitor or projector is getting power
    Check the connection at both ends of the video cable
    Is the monitor or projector turned on?
    Use the function keys on a laptop to toggle between the laptop display and the external monitor or projector
    Try using a different video cable
    Try using a different video connection if the laptop and monitor have another option available
    If the projector shuts off unexpectedly, it might have entered sleep mode due to inactivity

## Slide 59: Video System in a Laptop (1 of 5)
If LCD panel shows a black screen but power light is on:
  Look for an LCD cutoff switch or button on laptop
  Try to use the video port on the laptop to connect to an external monitor
  If external monitor does work, problem is with the LCD panel assembly
    Will need to replace inverter or LCD panel

## Slide 60: Video System in a Laptop (2 of 5)
Flickering, Dim, or Otherwise Poor Video
  Tips to solve problems with bad video:
    Verify Windows display settings
    Adjust the brightness
    Update the video drivers
    If the cursor drifts on the screen when the mouse or touch pad isn’t being used, try using a different port on the computer or replacing the batteries in the mouse
    A flickering screen can be caused by bad video drivers, a low refresh rate, a bad inverter, or loose connections inside the laptop

## Slide 61: Video System in a Laptop (3 of 5)
Replace the LCD Panel in a Laptop
  If LCD display is entirely black, replace LCD assembly
  If LCD display is dim, the video inverter might be the problem
    Check with manufacturer before replacing the LCD panel
  General directions to replace an LCD panel:
    Remove AC adapter and battery pack
    Remove the upper keyboard bezel and possibly, the keyboard
    Remove screws holding hinge in place and remove hinge cover
    Remove screws holding LCD panel to the laptop
    Remove LCD panel from the laptop
    Remove screws holding the top cover and LCD panel
    Disconnect old inverter and install the new one
    Reattach LCD panel assembly to the laptop

## Slide 62: Video System in a Laptop (4 of 5)
Figure 6-60 The inverter is exposed and is compared with the new one

## Slide 63: Video System in a Laptop (5 of 5)
Figure 6-61 Lift up on the ZIF connector locking mechanism before removing the ribbon cable

## Slide 64: Customizing Computer Systems
Important principles when customizing a system to meet customer needs:
  Meet application requirements
  Balance functionality and budget
  Consider hardware compatibility

## Slide 65: Graphics or CAD/CAM Design Workstation (1 of 2)
Graphics-intensive, advanced applications perform complex calculations, use large and complex files, and can benefit from the most powerful workstations
  Because 3D graphics is a requirement, a high-end or ultra-high-end video card is needed
Requirements for high-end workstations:
  Motherboard that provides at least dual channels for memory and plenty of memory slots, and generous amounts of RAM
  Powerful multicore processor with a large CPU cache
  Fast hard drives with plenty of capacity
  High-end video card

## Slide 66: Graphics or CAD/CAM Design Workstation (2 of 2)
Figure 6-62 A high-end CAD workstation customized for maximum performance

## Slide 67: Audio and Video Editing Workstation (1 of 2)
Audio- and video-editing applications are not usually as power-hungry as CAD/CAM and graphics applications
  You can get by with a less expensive graphics card and processor
What you need for a mid-range to high-end audio/video editing workstation:
  Core i7 equivalent or higher processor
  High-end motherboard
  At least 16 GB of RAM
  Video card with a GeForce GTX graphics processor or better
  Audio card for higher-quality sound output
  Maximum storage space
  Double-sided, dual-layer DVD burner and possibly a Blu-ray burner

## Slide 68: Audio and Video Editing Workstation (2 of 2)
Figure 6-64 This mid-range video-editing workstation uses a Core i7 processor and GTX graphics processor

## Slide 69: Gaming PC (1 of 2)
Gaming computers benefit from a powerful multicore processor designed for gaming, a high-end video card, and a high-definition sound card
Gamers might want to overclock their CPUs or use dual video cards
  Take extra care to make sure the cooling methods are adequate
Most gaming computers use onboard surround sound
  Or you can use a sound card to improve sound

## Slide 70: Gaming PC (2 of 2)
Figure 6-65 A group of Intel Core i7 gaming PCs

## Slide 71: NAS (Network Attached Storage) Device (1 of 2)
NAS devices can be used to serve up files and to stream media files and movies to client computers
Features and hardware you need to consider when customizing a NAS device:
  Processor with moderate power
  RAID array
  Appropriately sized chassis
  Gigabit NIC
  Media streaming capability

## Slide 72: NAS (Network Attached Storage) Device (2 of 2)
Figure 6-66 An eight-bay NAS device

## Slide 73: Chapter Summary (1 of 3)
Adding new devices to a computer require installing hardware and software
Use Device Manager to manage hardware devices and solve problems with them
Wired data transmission types include USB, eSATA, Thunderbolt, and Lightning
  Wireless data transmission types include Wi-Fi, Bluetooth, and NFC
USB connectors include A-Male, B-Male, Mini-B, Micro-B, and USB-C
Popular I/O ports on a motherboard include eSATA and USB
Video ports that a video card or motherboard might provide are VGA, DVI-I, DVI-D, DisplayPort, HDMI, HDMI mini, and multipurpose Thunderbolt ports

## Slide 74: Chapter Summary (2 of 3)
When installing devices, use 32-bit drivers for a 32-bit OS and 64-bit drivers for a 64-bit OS
A touch screen is likely to use a USB port
Biometric input devices collect biological data in order to authenticate access to a system
A KVM switch lets you use one keyboard, monitor, and mouse with multiple computers
Generally, Windows detects new adapter cards and installs appropriate drivers
Types of monitors include LCD and OLED
Use the Windows 10 Settings app or the Windows 8/7 Screen Resolution window to configure monitor resolution and configure dual monitors

## Slide 75: Chapter Summary (3 of 3)
Use Device Manager to update drivers on I/O devices giving trouble
Video problems can be caused by the monitor, video cable, video card, onboard video, video drivers, or Windows display settings
A few dead pixels on an LCD monitor screen are considered acceptable by the manufacturer
Artifacts on the monitor screen can be caused by hardware, software, overheating, or overclocking
As a technician, you might be called on to customize a system for a customer
A high-end video card is a requirement in a graphics, CAD/CAM, or video-editing workstation, or for a gaming PC