## Slide 1: CompTIA A+ Guide to IT Technical Support
10th Edition

## Slide 2: Setting Up a Local Network
Chapter 7

## Slide 3: Objectives
Describe network types and the Internet connections they use
Connect a computer to a wired or wireless network
Configure and secure a multifunction router on a local network
Troubleshoot network connections using the command line

## Slide 4: Types of Networks and Network Connections
Networks can be categorized by technology used and size of the network
  PAN (personal area network): consists of personal devices such as a cell phone and laptop
  LAN (local area network): covers a small local area such as a home, office, or other building
  WMN (wireless mesh network): covers a limited geographic area and is popular in places where cables are difficult to install
  MAN (metropolitan area network): covers a large campus or city
  WAN (wide area network): covers a large geographic area and is made up of small networks

## Slide 5: Internet Connection Technologies (1 of 13)
Internet Service Provider (ISP): used to connect to the Internet
  Most common type of connections are DSL and cable Internet (cable modem)
  ISPs devote more available bandwidth to downloading and less of it to uploading
Bandwidth: measure of the maximum data transmission rate
Data throughput: actual network transmission speed
Latency: delays in network transmissions
  Measured by the round-trip time it takes for a data packet to travel from source to destination and back

## Slide 6: Internet Connection Technologies (2 of 13)
Figure 7-1 An ISP stands between a LAN and the Internet

## Slide 7: Internet Connection Technologies (3 of 13)
Compare Cable Internet and DSL
  Cable Internet
    Uses existing TV cable lines and is always connected (always up)
    TV signals and PC data signals share the same coax cable
    Cable modem converts PC’s digital signals to analog
      And converts incoming analog data to digital
  DSL (Digital Subscriber Line)
    A group of broadband technologies that covers a wide range of speeds
    Uses ordinary copper phone lines and unused voice frequencies
    Always connected
    Can use the same phone line for voice and DSL at the same time

## Slide 8: Internet Connection Technologies (4 of 13)
When deciding between cable Internet vs. DSL:
  Both can sometimes be purchased on a sliding scale
  Cable modem shares TV cable infrastructure with neighbors
    Service may become degraded
  DSL uses dedicated phone line
    Must filter phone line static
  Similar setup for both

## Slide 9: Internet Connection Technologies (5 of 13)
Figure 7-2 When DSL is used in your home, filters are needed on every phone jack except the one used by the DSL modem

## Slide 10: Internet Connection Technologies (6 of 13)
Figure 7-4 Use a cable modem to connect the ISP’s coaxial cable to the LAN’s Ethernet cable

## Slide 11: Internet Connection Technologies (7 of 13)
Dedicated Line Using Fiber Optic
  Fiber optic is a dedicated point-to-point (PTP) connection
    No line sharing
    Television, Internet data, and voice communication all share the broadband fiber-optic cable
    Upstream and downstream speeds and prices vary
Satellite
  Satellite provides high-speed Internet connections in remote areas
  Available everywhere (even airplanes)
  Disadvantages: requires line-of-site wireless connectivity and latency occurs when uploading

## Slide 12: Internet Connection Technologies (8 of 13)
Dial-Up
  Dial-up or POTS (plain old telephone service) is the least expensive and slowest connection to the Internet
Cellular WAN
  A wireless wide area network (WWAN), also called a cellular network or cellular WAN, covers a wide area
  Made up of cells created by base stations
  A base station might include more than one transceiver and antenna on the same tower
    To support multiple technologies
  Two established cellular technologies are GSM and CDMA
  Long Term Evolution (LTE) and Voice over LTE (VoLTE) are expected to ultimately replace GSM and CDMA

## Slide 13: Internet Connection Technologies (9 of 13)
Cellular WAN (continued)
  To connect a computer using mobile broadband to a cellular network, you need the hardware and software to connect and, for most networks, a SIM (Subscriber Identification Module) card
  Options for software and hardware devices that can connect to a cellular network:
    Embedded mobile broadband modem
    Cell phone tethering
    USB broadband modem
    LTE installed Internet
    Mobile hotspot

## Slide 14: Internet Connection Technologies (10 of 13)
Figure 7-6 A cellular WAN is made up of many cells that provide coverage over a wide area

## Slide 15: Internet Connection Technologies (11 of 13)
Figure 7-7 A SIM card contains proof that your device can use a cellular network

## Slide 16: Internet Connection Technologies (12 of 13)
Figure 7-8 Tether your laptop to your cell phone using a USB cable

## Slide 17: Internet Connection Technologies (13 of 13)
Figure 7-9 A USB broadband modem by Sierra Wireless

## Slide 18: Connecting a Computer to a Local Network
Connecting a laptop or desktop computer to a network is quick and easy in most situations
Topics covered in this section:
  How to connect to a wired or wireless network
  How to connect to a VPN

## Slide 19: Connecting to an Ethernet Wired or Wi-Fi Wireless Local Network (1 of 6)
To connect a computer to a network using a wired or wireless connection, follow these steps:
  1. Install network adapter and drivers
  2. For a wired network:
    Connect network cable to Ethernet RJ-45 port and network port
    Verify lights
    Windows should automatically configure connection
  For a wireless network:
    Click the Network icon and select a wireless network, click Connect
    If network is secured, must enter a security key

## Slide 20: Connecting to an Ethernet Wired or Wi-Fi Wireless Local Network (2 of 6)
To connect a computer to a network using a wired or wireless connection, follow these steps (continued):
  3. If this is the first time you’ve connected to a local network, you will be asked if you want to make the PC discoverable
    For private networks, click Yes and for public networks, click No
  4. Open browser and verify Internet connectivity
    For some hotspots, an initial page (called a captive portal) appears and you must enter a code or agree to the terms of use
    On a private network, open File Explorer or Windows Explorer and drill down into the Network group to verify that network resources are available
    To view and change network security settings in Windows 10, open the Setting app and click Network & Internet
      Click Change connection properties, and then select either Public or Private

## Slide 21: Connecting to an Ethernet Wired or Wi-Fi Wireless Local Network (3 of 6)
Figure 7-12 File Explorer shows resources on the network

## Slide 22: Connecting to an Ethernet Wired or Wi-Fi Wireless Local Network (4 of 6)
For wireless connections, view the status of the connection:
  1. Open Control Panel and open Network and Sharing Center
    Click Change adapter settings and the Network Connections window appears
  2. In the Network Connections window, right-click the Wi-Fi connection and click Status
    In the Wi-Fi Status box, click Wireless Properties, select the Security tab
    To view the security key, check Show characters
If you have a problem making a network connection, you can reset the connection
  Open the Network Connections window and right-click the network connection
  Select Disable from the shortcut menu
  Right-click the connection again and select Enable

## Slide 23: Connecting to an Ethernet Wired or Wi-Fi Wireless Local Network (5 of 6)
Figure 7-15 Verify that the Network security key for the wireless network is correct

## Slide 24: Connecting to an Ethernet Wired or Wi-Fi Wireless Local Network (6 of 6)
Figure 7-16 To repair a connection, disable and then enable the connection

## Slide 25: Creating a VPN Connection (1 of 3)
A virtual private network (VPN) is used by telecommuting employees to connect to a corporate network by way of the Internet
  Data is encrypted using a technique called a tunnel or tunneling
The VPN can be managed by operating systems, routers, or third-party software
VPN connection is a virtual connection
  Setting up a tunnel over an existing connection
When creating a VPN connection, always follow directions given by the network administrator who hosts the VPN

## Slide 26: Creating a VPN Connection (2 of 3)
General steps to connect to VPN using Windows:
  1. In Network and Sharing Center, click Set up a new connection or network, click Connect to a workplace – Set up a dial-up or VPN connection to your workplace, click Next
  2. In the Connect to a Workplace box, click Use my Internet connection (VPN), enter IP address or domain name of the network, name the VPN connection and click Create
Whenever you want to use the VPN connection, click the Network icon in the taskbar
  In the list of available networks, click the VPN connection and click Connect
  Enter your user name and password and click OK
Problems connecting to a VPN can be caused by the wrong authentication protocols used when passing the user name and password
  Click on the Properties of the VPN Connection to configure security settings

## Slide 27: Creating a VPN Connection (3 of 3)
Figure 7-21 Configure the VPN’s security settings

## Slide 28: Creating a Dial-Up Connection (1 of 2)
Bare-bones installation steps:
  Install internal or external dial-up modem
  Plug phone line into computer modem port and wall jack
  Open Network and Sharing Center window, click Set up a connection or network, select Connect to the Internet - Set up a broadband or dial-up connection, click Next
  Click Dial-up, enter ISP information, click Create
To use the connection:
  Click your Network icon in the taskbar
    Select dial-up connection, click Connect, click Dial
    You will hear modem dial up the ISP and make the connection

## Slide 29: Creating a Dial-Up Connection (2 of 2)
Figure 7-23 (A) Select your dial-up connection, and (B) enter the password to your ISP

## Slide 30: Dynamic and Static IP Configurations (1 of 4)
Computers use IP addresses to find each other on a network
An IP address is assigned to a network connection when the connection is first made and can be:
  A 32-bit string, written as four decimal numbers called octets and separated by periods
  A 128-bit string, written as eight hexadecimal numbers separated by colons
Most networks use 32-bit IP addresses
  Defined by IPv4 (Internet Protocol version 4)
Some networks use both 32-bit addresses and 128-bit addresses
  128-bit addresses are defined by IPv6 (Internet Protocol version 6)

## Slide 31: Dynamic and Static IP Configurations (2 of 4)
A host is any device on a network that requests or serves up data or services to other devices
To communicate on a network or the Internet, a host needs:
  Its own IP address – for example, 192.168.100.4
  A subnet mask – for example, 255.255.255.0
  The IP address of a default gateway, which is used to send data to other networks
  The IP address of one or more DNS (Domain Name System) servers
The above information can be manually assigned to a computer’s network connection
  The computer’s IP address would then be called a static IP address
This information can be requested from a server on the network (called a DHCP or Dynamic Host Configuration Protocol server)
  IP address received is called a dynamic IP address

## Slide 32: Dynamic and Static IP Configurations (3 of 4)
To configure dynamic and static IP addresses:
  Open Network Connections window, right-click network connection and select Properties
  On properties box, click Networking tab
  Select Internet Protocol Version 4 (TCP/IPv4) and click Properties
  Default setting is dynamic IP addressing
  To change to static select Use the following IP address
    Enter IP address, subnet mask, and default gateway
    If your network administrator has given you the IP addresses of DNS server, select Use the following DNS server addresses and enter up to two IP addresses

## Slide 33: Dynamic and Static IP Configurations (4 of 4)
Figure 7-25 Set static IP addressing information in the Settings app

## Slide 34: Alternate IP Address Configuration (1 of 2)
If using a laptop that moves from one network to another and one network uses static:
  Use the General tab of the TCP/IPv4 Properties box
  Click Alternate Configuration tab and select User configured to enter static IP address information
  Click OK and close all boxes

## Slide 35: Alternate IP Address Configuration (2 of 2)
Figure 7-26 Create an alternate static IP address configuration

## Slide 36: Managing Network Adapters (1 of 2)
A computer makes a wired or wireless connection to a local network using a network adapter
  It might be a network port on the motherboard or a network interface card (NIC)
  It may also be an external device connected via a USB port
Features to be aware of on an adapter:
  The drivers a NIC uses
  Ethernet speeds
    Full duplex sends and receives transmissions at the same time
    Half duplex works in only one direction at a time
  MAC address – every network adapter has one
    48-bit unique ID number hard-coded by manufacturer

## Slide 37: Managing Network Adapters (2 of 2)
Features to be aware of on an adapter (continued):
  Status indicator lights
  Wake-on-LAN – wakes up the computer when it receives certain communication on the network
    For an onboard NIC, you must enable Wake-on-LAN in BIOS/UEFI setup
  Quality of Service (QoS)
    Ability to control which applications have priority on the network
    Must be configured on the router and the network adapter of each computer

## Slide 38: Setting Up a Multifunction Router for a SOHO Network
In order to setup a SOHO (small office or home office) network you need to know:
  How to configure a multipurpose router to stand between the network and the Internet
A router is a device that manages traffic between two or more networks
  Can help find the best path for traffic to get from one network to another

## Slide 39: Functions of a SOHO Router
A typical SOHO router usually combines these features:
  As a router, it stands between the ISP network and the local network, routes traffic between
  As a switch, it manages several network ports that can be connected to wired computers or other network devices
  As a DHCP server, all computers receive their IP address from this server
  As a wireless access point (WAP), a wireless computer can connect to the Internet
  As a firewall, it blocks unwanted traffic from the Internet and can restrict Internet access for local devices behind the firewall
  If the router is used as an FTP (File Transfer Protocol) server, you can connect an external hard drive and FTP firmware on router can be used to share files with network users

## Slide 40: Installing and Configuring a Router on the Local Network (1 of 3)
When deciding where to physically place a router, consider its physical security
  For best security, place the router behind a locked door accessible only to authorized personnel
  Also, make sure it is centrally located to create the best Wi-Fi hotspot for users
For routers that have external antennas, raise the antennas to vertical positions
General steps to configure a router:
  1. Open browser and enter IP address of router
    Enter admin as the user name (or whatever user name is assigned)
  2. Use menus on the main setup page of the router firmware to change router’s configuration
    Every router is different so poke around until you find the setting you need to configure
    When finished, save changes, click Logout, and close browser window

## Slide 41: Installing and Configuring a Router on the Local Network (2 of 3)
Figure 7-39 The main screen for router firmware setup

## Slide 42: Installing and Configuring a Router on the Local Network (3 of 3)
Changes you might need to make to the router’s configuration:
  Change the router password
  Configure the DHCP server
  Reserve IP addresses
  MAC address filtering
  QOS for an application or device
  Universal Plug and Play (UPnP)
  Update router firmware

## Slide 43: Limiting Internet Traffic on Your Network (1 of 8)
A router’s firewall can examine each message coming from the Internet
  Decides if the message is allowed onto the network
A message is directed to a particular computer and to a particular application running on that computer
  The application is identified by a port number, also called a port or port address
Routers offer the option to disable (close) all ports
  Means no activity from the Internet can get in
  You must specify exceptions to this firewall rule in order to allow unsolicited traffic from the Internet
Exceptions are allowed using port forwarding or a DMZ

## Slide 44: Limiting Internet Traffic on Your Network (2 of 8)
Figure 7-48 Each server application running on a computer is addressed by a unique port number

## Slide 45: Limiting Internet Traffic on Your Network (3 of 8)
Port Forwarding
  Port Forwarding: when a firewall receives a request for communication from the Internet to a specific computer and port, the request will be allowed and forwarded to that computer
Tips when using port forwarding:
  You must lease a static IP address from your ISP
  For port forwarding to work, the computer on your network must have a static IP address
  Using port forwarding, your computer and network are more vulnerable
    You are allowing external users directly into your private network

## Slide 46: Limiting Internet Traffic on Your Network (4 of 8)
Figure 7-49 Port forwarding on a network

## Slide 47: Limiting Internet Traffic on Your Network (5 of 8)
Figure 7-50 Using port forwarding, activity initiated from the Internet is allowed access to a computer on the network

## Slide 48: Limiting Internet Traffic on Your Network (6 of 8)
Figure 7-51 With port forwarding, a router allows messages past the firewall that are initiated outside the network

## Slide 49: Limiting Internet Traffic on Your Network (7 of 8)
DMZ
  A DMZ (demilitarized zone) is a computer or network that is not protected by a firewall
    If having problems getting port forwarding to work, put it in the DMZ zone
Content Filtering and Parental Controls
  Routers normally provide a way for employers and parents to limit the content computers on the local network can access on the Internet
    Can apply to specific computers, users, websites, categories of websites, keywords, services, time of day, and day of week
  Criteria for filtering can draw from blacklists (lists of what cannot be accessed) or whitelists (lists of what can be accessed)

## Slide 50: Limiting Internet Traffic on Your Network (8 of 8)
Figure 7-53 Block sites by keyword or domain names

## Slide 51: Setting Up a Wireless Network (1 of 7)
Wi-Fi (Wireless Fidelity) standards have evolved over the years
  Technical name is IEEE 802.11 standards
Wi-Fi standards:
  802.11a – range up to 50 meters and radio frequency of 5.0 GHz
  802.11b – range of 100 meters and radio frequency of 2.4 GHz
  802.11g – same range and frequency as 802.11b but with faster speeds up to 54 Mbps
  802.11n – uses either 5.0-GHz or 2.4-GHz frequency with an indoor range up to 70 meters and outdoor range up to 250 meters
  802.11ac – uses the 5.0-GHz frequency and has the same ranges as 802.11n, except performance stays stronger at the edges of its reach

## Slide 52: Setting Up a Wireless Network (2 of 7)
Figure 7-54 A wireless network adapter with two antennas supports 802.11a/b/g/n/ac Wi-Fi standards

## Slide 53: Setting Up a Wireless Network (3 of 7)
Security Key
  Most common and effective method of securing a wireless network is to require a security key
  Data is encrypted using an encryption standard
  Use the router firmware to set the security key
  Best to enter a security key that is different from the password you use to the router utility

## Slide 54: Setting Up a Wireless Network (4 of 7)
Set Encryption
  The main security standards for 802.11 wireless networks:
    WEP (Wired Equivalent Privacy) – no longer considered secure because key used for encryption is static
    WPA (Wi-Fi Protected Access) – also called TKIP and is stronger than WEP because encryptions keys are constantly changing
    WPA2 (also called 802.11i standard) – latest and best encryption standard
    WPA3 offers better encryption and additional features over WPA2

## Slide 55: Setting Up a Wireless Network (5 of 7)
Change the Default SSID and Disable SSID Broadcasting
  The Service Set Identifier (SSID) is the name of the wireless network
  Not considered a strong security method because software can be used to discover an SSID that is not broadcasted
Select Channels for the WLAN
  Channel: a specific radio frequency within a broader frequency
    In the US, 11 channels are available for wireless networks
    If experiencing interference, you can set each network to a different channel
Radio Power Levels
  Some high-end APs allow you to adjust radio power levels to reduce interference, limit the range of the network, or to save on electricity

## Slide 56: Setting Up a Wireless Network (6 of 7)
Figure 7-56 Select a channel in the 2.4-GHz band

## Slide 57: Setting Up a Wireless Network (7 of 7)
Wireless QoS
  For wireless devices, you can improve QoS by enabling WMM (Wi-Fi Multimedia)
  When WMM is enabled, the wireless access point will prioritize wireless traffic for audio, video, and voice over other types of wireless network traffic
Wi-Fi Protected Setup (WPS)
  Generates the SSID and security key using a random string of hard-to-guess letters and numbers
  WPS might be a security risk if not managed well
    Turn on auto disable so that WPS will disable after a few failed PIN entries

## Slide 58: Troubleshooting Network Connections
Windows includes several utilities you can use to troubleshoot networking problems:
  ping
  ipconfig
  nslookup
  tracert
  Two net commands
  netstat

## Slide 59: Ping [-A] [-T] [Targetname] (1 of 2)
The ping command tests connectivity by sending an echo request to a remote computer
  If the remote computer is online, detects the signal, and is configured to respond to a ping, it responds
Use ping to test for connectivity or to verify that DNS is working

## Slide 60: Ping [-A] [-T] [Targetname] (2 of 2)
Ping Command | Description
ping 69.32.208.75 | Ping tests for connectivity using an IP address. If the remote computer responds, the round-trip times are displayed.
ping –a 69.32.208.75 | The –a parameter tests for name resolution. Use it to display the host name and verify that DNS is working.
ping –t 69.32.208.75 | The –t parameter causes pinging to continue until interrupted. To display statistics, press Ctrl+Break. To stop pinging, press Ctrl+C.
ping 127.0.0.1 | This is called a loopback address test. The IP address 127.0.0.1 always refers to the local computer. If the local computer does not respond, you can assume there is a problem with the network connection’s configuration.
ping cengage.com | Use a host name to find out the IP address of a remote computer. If the computer does not respond, suspect there is a problem with DNS. On the other hand, some computers are not configured to respond to pings.

## Slide 61: Ipconfig [/all] [/release] [/renew] [/displaydns] [/flushdns] (1 of 2)
The ipconfig (IP configuration) command can display network configuration information
  And refresh the TCP/IP assignments for a connection

## Slide 62: Ipconfig [/all] [/release] [/renew] [/displaydns] [/flushdns] (2 of 2)
Ipconfig Command | Description
ipconfig /all | Displays a network connection’s configuration information, including the MAC address.
ipconfig /release | Releases the IP address and other TCP/IP assignments when dynamic IP addressing is being used.
ipconfig /release6 | Releases an IPv6 address and other TCP/IP assignments.
ipconfig /renew | Leases a new IP address from a DHCP server. Make sure you release the IP address before you renew it.
ipconfig /renew6 | Leases a new IPv6 address from a DHCP IPv6 server. Make sure you release the IPv6 address before you renew it.
ipconfig /displaydns | Displays information about name resolutions that Windows currently holds in the DNS resolver cache.
ipconfig /flushdns | Flushes the name resolver cache, which might solve a problem when the browser cannot find a host on the Internet.

## Slide 63: Nslookup [Computername] (1 of 2)
The nslookup (namespace lookup or name server lookup) command is used to test name resolution problems with DNS servers
  Allows you to request information from a DNS server’s zone data
Zone data is the portion of the DNS namespace that the server knows about
  A reverse lookup is when you use the nslookup command to find the host name when you know the IP address

## Slide 64: Nslookup [Computername] (2 of 2)
Figure 7-60 The nslookup command reports information about the Internet namespace

## Slide 65: Tracert [targetname] (1 of 2)
The tracert (trace route) command can be useful when trying to resolve a problem reaching a destination host
The command sends a series of requests to the destination computer and displays each hop to the destination
    A hop happens when a packet moves from one router to another
A message is assigned a Time To Live (TTL), which is the number of hop counts it can make before a router drops the packet and sends an ICMP message back to the host that sent packet

## Slide 66: Tracert [targetname] (2 of 2)
Figure 7-61 The tracert command traces a path to a destination computer

## Slide 67: The Net Commands
The net command is several commands in one
  Most require an elevated command prompt window
Net use command connects or disconnects a computer from a shared resource
Use the following command to pass a user name and password to the \\bluelight remote computer, and then map a network drive to the /Medical folder on that computer:
  net use \\bluelight\Medical /user:”Jean Andrews” mypassword
  net use z: \\bluelight\Medical
Net user command manages user accounts

## Slide 68: Netstat [-A] [-B] [-O] (1 of 2)
The netstat (network statistics) command gives statistics about network activity and includes several parameters

## Slide 69: Netstat [-A] [-B] [-O] (2 of 2)
Netstat Command | Description
netstat | Lists statistics about the network connection, including the IP addresses of active connections.
netstat >>netlog.txt | Directs output to a text file.
netstat –b | Lists programs that are using the connection and is useful for finding malware that might be using the network. The –b switch requires an elevated command prompt.
netstat –b –o | Includes the process ID of each program listed. When you know the process ID, you can use the taskkill command to kill the process.
netstat –a | Lists statistics about all active connections and the ports the computer is listening on.

## Slide 70: Chapter Summary (1 of 2)
Networks are categorized in size as a PAN, LAN, Wireless LAN, MAN, or WAN
Network performance is measured in bandwidth and latency
Two most popular ways to connect to the Internet are cable Internet and DSL
A VPN protects data by encrypting it from the time it leaves the remote computer until it reaches a server on the corporate network
A host needs an IP address, subnet mask, default gateway, and IP addresses for DNS servers to communicate with other hosts on the local or remote networks
Network adapters, commonly called NICs, are rated by speed and each has a MAC address

## Slide 71: Chapter Summary (2 of 2)
A multifunction router for a SOHO network might serve several functions including a router, a switch, a DHCP server, a wireless access point, a firewall, and an FTP server
Change the router’s password as soon as you install it
To allow certain traffic initiated from the Internet past your firewall, you can use port forwarding, a DMZ, and content filtering with whitelists or blacklists
To secure a wireless access point, require a security key, disable SSID broadcasting, and enable encryption (WPA2, WPA, or WEP)
Useful Windows command-line utilities for network troubleshooting are ping, ipconfig, nslookup, tracert, net use, net user, and netstat